## Slide 1
FOR RADIO ENGINEERS — HOW IT ACTUALLY WORKS
PrimeNet
KPIs, detections, CM & RET — the radio engineering inside the tool
Nokia + Huawei
2G · 3G · 4G · 5G
Hourly & daily PM
CM read + governed write
⟳ This is a companion deck. Amber bands mark live-tool checkpoints — keep PrimeNet open in a second window and switch whenever you see one.
Slides explain the logic behind each screen; the tool shows it running on your network.
Presenter: Malek Mohammad · Audience: RF / RAN optimization engineers

## Slide 2
PRESENTER GUIDE
How to run this session
The two-window rhythm
▸ Deck = the logic. Thresholds, formulas, and workflows the UI doesn't spell out — why a cell got flagged.
▸ Tool = your network. Every detection shown on a slide is then shown live, on real cells.
▸ Layout: deck on one half of the screen, PrimeNet on the other — or two monitors.
▸ Cadence: explain one detection → amber checkpoint → find a real example live → back to deck.
▸ Login before starting and keep a busy area in mind — live examples land better than slides.
SLIDE LEGEND
⟳ SWITCH TO TOOL
Stop talking, start clicking. Click-path is monospaced.
Point out
What the audience must notice on the live screen.
▸ blue bullets
The radio logic — thresholds, weights, evidence.
formula cards
The actual scoring math the tool runs, verbatim.
No live network? The deck stands alone — every checkpoint has enough context to narrate.
PrimeNet · RAN Engineering Deep-Dive
Presenter guide
01

## Slide 3
ROADMAP
What we'll cover
01
Your day in PrimeNet
The monitor → detect → diagnose → change → verify loop
02
The data underneath
PM cadence, sources, metadata — what "latest" means
03
KPIs across two vendors
Recipes & aliases: one KPI name, per-vendor counters
04
How issues are scored
Severity, evidence, and reading an issue card
05
The detections, in depth
Sleeping cells · overshooting · neighbors · capacity
06
CM: reading the network
MO trees, live vs plan config, parameter dictionary
07
Audits, changes & RET
Golden-parameter audit, change impact, safe tilt writes
08
The daily loop & trust
Morning report, sector health, data freshness
PrimeNet · RAN Engineering Deep-Dive
Roadmap
02

## Slide 4
SECTION 01
Your day in PrimeNet: one optimization loop
MONITOR
Morning Report Sector Health Network Map / Heatmap
→
DETECT
Sleeping Cells Overshooting Capacity Hotspots Neighbor Quality
→
DIAGNOSE
Performance Explorer KPI trends & evidence Parameter Dictionary
→
CHANGE
RET tilt / CM edits Excel mass-modify (plan first, then apply)
→
VERIFY
Change Impact Tracker Config History next-day KPIs
↺ Verify feeds Monitor — every applied change shows up in tomorrow's morning report and impact tracker.
▸ Everything is cell-level and evidence-backed. Each detection carries the KPI values that triggered it — no black-box 'AI says so'.
▸ Both vendors, one workflow. Nokia and Huawei cells appear in the same lists with the same severities; you don't switch tools per vendor.
▸ Reads are free, writes are staged. All analytics are read-only; tilt/parameter changes go through an explicit plan → apply → history flow.
PrimeNet · RAN Engineering Deep-Dive
01 · Workflow
03
⟳ SWITCH TO TOOL — live demo checkpoint
Show the dashboard: the module deck maps 1:1 to this loop.
Click path: Login → Dashboard (hover the Radio Optimization section)

## Slide 5
SECTION 02
The data underneath
Where the numbers come from
Nokia PM
NetAct exports over SFTP
hourly + daily
Huawei PM
U2020 exports over SFTP
hourly + daily
Metadata
site/cell inventory, azimuths, coords, on-air state
snapshot
▸ Hourly drives near-real-time views (sector health, busy-hour checks).
▸ Daily drives baselines and detections — a stable day-level series per cell.
▸ Metadata joins everything: cell → site, area, vendor, technology, azimuth, on-air state.
HOW PM IS ORGANIZED
per vendor nokia · huawei
per RAT 2G · 3G · 4G · 5G
(4G FDD/TDD share the 4G table)
per cadence hourly · daily
per scope cells · groups (clusters/areas)
KPI columns are detected automatically at
import — new counters in a vendor export
appear as new KPIs, no mapping to maintain.
Why you should care: every detection later in this deck runs on the daily per-cell series; if a day's file is late, that day is simply absent — the tool never interpolates fake data.
PrimeNet · RAN Engineering Deep-Dive
02 · Data
04

## Slide 6
SECTION 03
One KPI, two vendors: recipes & aliases
You ask for a concept ("utilization"); PrimeNet resolves the right per-vendor counter column automatically:
RECIPE
DIRECTION
HUAWEI COUNTERS (examples)
NOKIA COUNTERS (examples)
utilization
higher = worse
DL/UL PRB Usage Rate(%)
E-UTRAN Avg PRB usage per TTI DL
users
higher = worse
Average User Number · RRC Connected Users
Active Users
traffic
higher = worse
Traffic Volume · Payload
Data Volume · DL/UL Traffic
throughput
lower = worse
User/Cell Throughput
Average Throughput
accessibility / retainability / mobility / interference
category presets
vendor formulas per RAT
vendor formulas per RAT
Matching is normalized (case/punctuation-insensitive) per vendor + RAT — so cross-vendor comparisons like "top PRB utilization cells network-wide" are one query, not two exports and a VLOOKUP.
PrimeNet · RAN Engineering Deep-Dive
03 · KPIs
05
⟳ SWITCH TO TOOL — live demo checkpoint
Query the same KPI across Nokia and Huawei cells in one screen.
Click path: Dashboard → Performance Explorer → vendor: All → pick a KPI → Top-N

## Slide 7
SECTION 04
How issues are scored (read this once, use it everywhere)
▸ Additive, capped signals. Each detection sums a few capped penalty terms; the total is clipped to 0–100.
▸ Severity is just a banding of the score — same thresholds in every module (right).
▸ Evidence rides along. Every issue carries the raw KPI values (pre / post / delta, dates, distances) that produced its score.
▸ Stable identity. The same cell + problem keeps the same issue ID across days — you can track it until it's fixed.
SEVERITY BANDS (ALL MODULES)
Critical
≥ 85
High
≥ 70
Medium
≥ 45
Low
> 0
Info
0
ANATOMY OF AN ISSUE CARD
Sleeping cell AMM0416_L18_1
Critical · score 92 · Availability · Huawei · 4G
"CM state Active but 'Traffic Volume' flatlined for 3 day(s):
latest=0.01 vs baseline avg 412.6 over previous 7 day(s)"
evidence: { kpi, days_asleep, baseline_avg,
quiet_cutoff, recent[], baseline[] }
recommendation: check alarms, TX path, RET/RRU,
transmission — likely silent outage or barred cell
Title → what · Summary → why · Evidence → proof · Recommendation → next action
PrimeNet · RAN Engineering Deep-Dive
04 · Scoring
06

## Slide 8
SECTION 05
Detection 1 — Sleeping cells
Definition: a cell that is on-air per CM (activity = Active) but whose daily traffic collapsed to ~zero against its own baseline — a silent outage no alarm caught.
▸ Baseline = the cell's own history. 7 previous days of daily traffic (or users, if no traffic KPI exists for that table).
▸ Recent window = last 2 days. The cell is a candidate only if its best recent day is still below the quiet cutoff.
▸ Quiet cutoff is relative: 2% of the baseline average, floored at 0.05 — a small cell isn't flagged for being small.
▸ Low-traffic cells excluded: baseline average < 1.0 (KPI units) is ignored — nothing meaningful to lose.
▸ Days-asleep counts back consecutive quiet days from the newest sample — it can exceed the 2-day window.
SCORE (0–100)
score = 45 # base: it IS asleep
+ min(25, √baseline_avg) # bigger cell,
# bigger loss
+ min(30, days_asleep×10) # longer = worse
quiet_cutoff = max(0.05, 0.02 × baseline_avg)
Reading it: a busy cell (baseline 400+) asleep 3 days lands ≈ 45+20+30 = 95 → Critical. A quiet rural cell asleep 1 day ≈ 45+3+10 = 58 → Medium.
PrimeNet · RAN Engineering Deep-Dive
05 · Detections
07
⟳ SWITCH TO TOOL — live demo checkpoint
Open Sleeping Cells; expand one issue and show recent[] vs baseline[] in the evidence.
Click path: Dashboard → Radio Optimization → Sleeping Cell Detector
Point out: CM says Active, PM says dead — that gap is the whole detection.

## Slide 9
SECTION 05
Detection 2 — Overshooting
Definition: a cell handing over to neighbors far beyond its intended footprint — serving where it shouldn't, degrading HO performance and polluting the far cell's area.
▸ Source: the HO relation matrix. Per source→target neighbor line: attempts, failures, success rate, inter-site distance (min 5 attempts to count).
▸ Distance gate: relations under 8 km are ignored — normal grid geometry, not overshooting.
▸ Three penalty terms: distance beyond 8 km, HO failure ratio, and HO success rate below 95%.
▸ Keep threshold: score < 30 is dropped — only actionable candidates surface.
▸ First-pass heuristic by design: needs no TA/MR/RSRP data; confirm with TA or drive-test evidence before tilting.
SCORE (0–100)
if distance < 8 km: skip
score = min(45, (distance − 8) × 4)
+ min(25, failures/attempts × 100)
+ max(0, 95 − HO_success_rate)
keep if score ≥ 30
Action path: evidence includes source azimuth → check the bearing, then downtilt (RET module), power, or clean the neighbor plan. 15 km + failing HOs ≈ 28+x → strong candidate.
PrimeNet · RAN Engineering Deep-Dive
05 · Detections
08
⟳ SWITCH TO TOOL — live demo checkpoint
Sort by score; pick a candidate and cross-check its azimuth & distance on the map.
Click path: Radio Optimization → Overshooting Detector → Network Map (same cell)
Point out: Far-target distance + failure ratio in the evidence block — then the geometry on the map.

## Slide 10
SECTION 05
Detection 3 — Neighbor quality
Every defined neighbor relation is scored by summing independent penalties — one bad relation can fail for several reasons at once:
SIGNAL
PENALTY
READING IT
Poor HO success
(95 − SR) × 1.4
SR 88% → 9.8 pts; missing SR data → flat 10
HO failures
min(35, fail/attempts × 100)
failure ratio capped at 35 pts
Excessive distance
+20 if ≥ 12 km
geometry sanity check on the relation
Missing reciprocal
+15 if B→A not defined
one-way neighbors break return mobility
Cross-vendor edge
+8 if vendors differ
Nokia↔Huawei borders need extra attention
Relations need ≥10 HO attempts to be judged; total score < 25 is discarded. Summary strings are engineer-readable: "HO SR 88.2%, 214 failed HOs, missing reciprocal, 14.1 km"
PrimeNet · RAN Engineering Deep-Dive
05 · Detections
09
⟳ SWITCH TO TOOL — live demo checkpoint
Filter to one area; show a relation failing on multiple penalties at once.
Click path: Radio Optimization → Neighbor Quality Analyzer → area filter

## Slide 11
SECTION 05
Detections 4 & 5 — Capacity hotspots · Layer gaps
CAPACITY HOTSPOTS
Finds cells whose PRB utilization is both rising and already high — growth pressure, not a one-day spike.
SCORE
delta = |latest − baseline| utilization
score = min(45, delta × 2)
+ max(0, latest − 70) × 1.2
keep if score ≥ 20
The 70% knee: below ~70% PRB, users rarely feel it; each point above 70 adds 1.2 pts. Recommendation: busy-hour PRB/users review → carrier add or sector split.
LAYER COVERAGE GAPS
Inventory-based (no PM needed): per sector, which technology layers exist vs which the grid design expects.
SCORE
+35 if LTE missing entirely
+20 if 3G missing
+min(35, missing_layers × 7)
(per absent LTE band, e.g. L18/L21)
Use it for: finding sectors where a band was never integrated, decommissioned by mistake, or metadata is stale — validate design before chasing 'coverage complaints'.
PrimeNet · RAN Engineering Deep-Dive
05 · Detections
10
⟳ SWITCH TO TOOL — live demo checkpoint
Show a hotspot cell's utilization trend, then a sector with a missing band.
Click path: Capacity Hotspots → evidence · then Layer Coverage Gaps

## Slide 12
SECTION 06
CM: reading the live network
▸ Live config on demand. PrimeNet reads current parameter values straight from the OSS — NetAct for Nokia, U2020 for Huawei — not from a stale weekly export.
▸ The MO tree is your address system. Nokia: PLMN → RNC/BSC → WBTS/WCEL (3G), MRBTS → LNCEL (4G). Every cell/parameter has one distinguished name (DN).
▸ Live vs plan. Reads target the actual network; writes go to a plan configuration first — nothing edits live directly.
▸ Huawei side speaks MML. The same UI drives LST/MOD commands under the hood; responses are parsed into the same tables.
▸ Parameter Dictionary: ~19,000 Huawei parameter reference pages searchable offline — meaning, range, impact, before you touch anything.
ONE CELL, TWO VENDORS
Nokia (3G cell):
PLMN-PLMN/RNC-521/WBTS-176/WCEL-1
class NOKRNC:WCEL — read via CM API
Huawei (4G cell):
LST CELL: LOCALCELLID=1;
MOD CELLALGOSWITCH: … ;
MML over U2020 — parsed to same table
→ same grid in the UI, vendor hidden
Exports land as Excel — the same file format the mass-modify flow re-imports.
PrimeNet · RAN Engineering Deep-Dive
06 · CM
11
⟳ SWITCH TO TOOL — live demo checkpoint
Extract one site's cells; open the Excel; look up one parameter in the dictionary.
Click path: Configuration → Configuration Data Extractor → site scope → Extract · Parameter Dictionary

## Slide 13
SECTION 07
CM Parameter Audit & Change Impact
GOLDEN-PARAMETER AUDIT
You define the golden config as rules; the tool scans the latest CM snapshot and flags every violation.
equals
value must match expected (e.g. qRxLevMin = -128)
range
numeric bounds (e.g. 0 ≤ tilt offset ≤ 10)
not_empty
parameter must be set at all
Rules carry vendor / RAT / MO-class scope and their own severity (Critical→90 … Low→30). Findings export to Excel for the change board.
CHANGE IMPACT TRACKER
Answers the morning-after question: did yesterday's parameter changes hurt anything?
1 Diff CM snapshots → list of parameter changes per cell
2 Pull the degraded-cells list from daily PM (accessibility, retainability…)
3 Correlate: change + degradation on the same cell → score 65; change alone → 35
4 Summary names both: "pci changed 101→237. PM degradation also seen in Retainability (−4.2%)"
PrimeNet · RAN Engineering Deep-Dive
07 · Audit & impact
12
⟳ SWITCH TO TOOL — live demo checkpoint
Run the audit on one vendor/RAT; then show a correlated change in Change Impact.
Click path: Configuration → CM Parameter Audit → Scan · Radio Optimization → Change Impact Tracker

## Slide 14
SECTION 07
RET: reading & changing tilts safely
▸ Read tilts across both vendors in one grid — current electrical tilt per antenna/RET unit, joined to cell & site metadata.
▸ Writes are explicit, never bulk-blind. You stage the target tilt per RET unit; the tool generates the vendor command (Huawei RET MOD / Nokia CM write).
▸ Value handling is vendor-aware. Tilt units, offsets, and command formatting differ per vendor — the tool normalizes so you type degrees, not vendor syntax.
▸ Every applied change is recorded in Config History: what, when, who, old → new — your rollback reference.
▸ Close the loop with Change Impact: tomorrow, the tilt change shows up correlated with its KPI effect.
TILT CHANGE — TYPICAL FLOW
1 Detect overshooting candidate at 14 km, azimuth 120°
2 Confirm map geometry + HO evidence + (TA if available)
3 Read current tilt: 2° electrical on that RET unit
4 Stage target 4° — review generated command
5 Apply execute; result logged to Config History
6 Verify next-day Change Impact + neighbor HO SR
PrimeNet · RAN Engineering Deep-Dive
07 · RET
13
⟳ SWITCH TO TOOL — live demo checkpoint
Read tilts for one site; stage (but don't apply) a change and show the generated command.
Click path: Configuration → RET Management → site filter
Point out: The vendor command preview — degrees in, vendor syntax out.

## Slide 15
SECTION 08
The daily loop: morning report & sector health
RADIO MORNING REPORT
▸ One overnight roll-up of every detection: sleeping cells, hotspots, neighbor issues, audit failures.
▸ Ranked by severity so the first 15 minutes of the day are triage, not hunting.
▸ Each line links back to its source module with evidence intact.
SECTOR HEALTH MONITOR
▸ Per-sector KPI composite across accessibility, retainability, mobility, interference.
▸ All-cells variant covers the whole network, with site names derived from cell names.
▸ Your drill-down surface when a report line needs context: is it one cell or the whole sector?
Trusting the numbers: data freshness is visible (per-vendor last-loaded day), missing days are shown as missing, and no KPI is ever interpolated. If the report looks quiet, check freshness before celebrating.
PrimeNet · RAN Engineering Deep-Dive
08 · Daily loop
14
⟳ SWITCH TO TOOL — live demo checkpoint
Open the morning report; follow one Critical line to its module and evidence.
Click path: Radio Optimization → Radio Morning Report → click a finding

## Slide 16
APPENDIX
End-to-end demo runbook (the full loop, live)
1
Morning Report
Start where the day starts — ranked overnight findings.
↳ Triage
2
Sleeping Cells
Drill into a Critical: recent[] vs baseline[] evidence.
↳ Detection logic
3
Performance Explorer
Trend the same cell's traffic KPI to confirm the flatline.
↳ KPI verification
4
Overshooting → Map
Pick a candidate; check azimuth & distance geometry.
↳ Diagnosis
5
RET Management
Read the tilt; stage the fix; show the vendor command.
↳ Change (staged)
6
CM Parameter Audit
Scan the same area against golden rules.
↳ Config hygiene
7
Change Impact
Show yesterday's changes correlated with PM deltas.
↳ Verification
≈ 20 minutes at demo pace. Steps 1–4 are safe anywhere; steps 5–7 stage changes only — nothing is applied during the demo.

## Slide 17
TAKEAWAYS
Evidence in, action out
▸ Every detection is explainable — fixed formulas, visible thresholds, raw KPI evidence on every issue card.
▸ Two vendors disappear — KPI recipes and CM adapters give you one workflow across Nokia and Huawei, 2G–5G.
▸ The loop closes — detect → diagnose → staged change → next-day impact, with Config History as the audit trail.
▸ Nothing is interpolated, nothing writes blind — missing data shows as missing; changes stage before they apply.
Questions? Name a site — let's run the loop on it live.